CP-545 BATTERY USAGE

8-2016

The CP-545 comes with rechargeable batteries. The setting for charging them is not always turned on. Make sure it is before relying on them later.

Charging status on upper left of screen

Select charge enabled

- Turn CP 545 on

- Press "F"

- Scroll down to "Parameters", Press Enter

- Scroll down to "Battery Type", Press Enter

- Scroll to NIMH charge enabled

- Highlight with arrow and Press Enter

- Press "F" twice to return to home screen

- You should see the battery indicator pulsing upwards and the AC adapter plug active

Use paper clip to reset if needed. Do not panic. Just insert paper clip and reset and try to start the timer again. You will need to do this if you change battery types.

DO NOT HAVE CHARGING ACTIVE IF YOU HAVE TO INSERT ALKALINE BATTERIES!!!

YOU WILL OVERHEAT THEM, CAUSE THEM TO BURST AND MAKE A BIG MESS, NOT TO MENTION VOID ANY WARRANTY

CHANGE THE BATTERY STATUS TO NO CHARGING

# SUPPORT

- THE Phoenix Sports Technology discussion forum is a great place to start:

- http://www.timingguys.com/6/ubb.x OR  www.timingguys.com

- Fred Patton can be reached on his worldwide cell phone at 610-972-5385

- The TAG HEUER  factory site has a great deal of information as well. You can download the latest manuals and brochures.

- www.tagheuer-timing.com